## Slide 1: Introduction to the Arduino
Pierce Nichols
10 January 2015
Presentation © Logos Electromechanical LLC 2015
CC BY-NC-SA-3.0

## Slide 2: Topics for Today
What is the Arduino?
Setting up your Arduino
Arduino IDE
Hello World!
Digital Output (blinking an LED)
Digital Input (responding to a button press)
Analog Input (sensing a potentiometer)
Expansion Boards (shields)
Image courtesy Sparkfun Electronics
CC BY-NC-SA-3.0

## Slide 3: Parts of the RedBoard
Image courtesy Sparkfun Electronics
CC BY-NC-SA-3.0

## Slide 4: Microcontroller: The brain of your Arduino
Miniature computer
  Processor
  Long-term storage (Flash)
  Short-term storage (RAM)
  Digital (binary) inputs and outputs
  Analog inputs
  Pulse-width modulated outputs (pseudo analog output)
Atmel ATMega328p
  16 MHz clock
  32 kB Flash memory for program storage
  2 kB RAM memory
  1 kB EEPROM
  14 digital input/output pins
  6 analog input pins

## Slide 5: Installing the IDE
Download Arduino 1.0.5 installer from http://arduino.cc/en/Main/Software
Follow driver installation instructions for Arduino Duemilanove if it doesn’t install automatically
Launch the IDE
Plug in your RedBoard

## Slide 6: Driver Installation
On many Windows and Linux installations, drivers are pre-installed and it just works. The Redboard will show up as a COM port (Windows) or a ttyUSB device (Linux and Mac)
On Macs and some Windows and Linux installations, you will need to install drivers.
  Download the VCP (Virtual COM Port) drivers for your system from http://www.ftdichip.com/Drivers/VCP.htm
  Follow the instruction on that page for your system

## Slide 7: Download the Slides & Examples
Go to the Github repository, https://github.com/logos-electromechanical/IntroToArduino/tree/master
If you have git set up on your machine, clone the repository.
Otherwise, download a zip file of the repository.

## Slide 8: Arduino IDE buttons

## Slide 9: Selecting you Board

## Slide 10: Hello World!
setup() function runs once at the beginning of program execution
loop() function is called repeatedly during program execution
Serial.begin() sets up the serial port and sets the speed.
Serial.println() prints a line to the serial port
delay() waits for the given number of milliseconds
See http://arduino.cc/en/Reference/HomePage for documentation of Arduino language constructs.

## Slide 11: Wiring for Blink

## Slide 12: Opening Blink Sketch…

## Slide 13: Blink Sketch Explanation
pinMode() sets the selected digital pin to either OUTPUT or INPUT. Pins default to INPUT.
digitalWrite() sets the selected pin either LOW or HIGH. Pins default to LOW.
delay() waits for the given number of milliseconds
What blinks other than the LED you added?
Play with adding more LEDs, different delay lengths, more complex sequences.

## Slide 14: Button Wiring

## Slide 15: Opening Button Sketch

## Slide 16: Button code explanation
digitalRead() returns the state of the named pin, either HIGH or LOW
If() and else() are branching statements – they allow the program to do different things depending on the input.

## Slide 17: Analog Input Wiring

## Slide 18: AnalogRead code
analogRead() returns the analog value from the given pin as a number between 0 and 1023

## Slide 19: Analog LED Control Wiring

## Slide 20: Analog LED Control Code
map() maps a value from one range to another. analogInput() returns a value between 0-1023 and analogOutput() takes a value from 0-255
analogWrite() simulates the given voltage by turning the target pin on and off quickly with a variable duty cycle.
Serial.print() prints a value or a string without adding a newline at the end.

## Slide 21: Pulse Width Modulation

## Slide 22: Expanding the Capabilities of the Arduino
Using external power supplies other than USB (DC jack, Vin pin)
Using shields – external expansion boards. Ethernet, LCDs, motor drivers, etc.

## Slide 23: Further Resources